## Slide 1
CSCI465 Introduction to Parallel Computing
AutoCluster-OMP
A Lightweight Source-to-Source OpenMP Auto-Parallelizer
for K-Means and Fuzzy C-Means Clustering
Research Team
Mohamed Yasser Goma
Abdullah Ismail
Mohamed Khaled
Mohamed Saleh
Ahmed Sayed
AutoCluster-OMP · Parallel Computing Research · 2025

## Slide 2
WHY THIS MATTERS
Motivation
Clustering at Scale
K-Means & Fuzzy C-Means are core to ML, data science, and pattern recognition — but runtime explodes with scale.
Multicore Potential
Modern CPUs have 8–64 cores. OpenMP unlocks them — but harnessing that power requires expertise.
Manual Parallelization
Developers must manually identify safe loops, understand data dependencies, and avoid race conditions.
Automation Opportunity
Source-to-source auto-parallelization can generate correct OpenMP code without manual effort.
02

## Slide 3
THE CHALLENGE
Problem Statement
01
Manual Loop
Identification
02
Safety
Analysis
03
Race Condition
Risk
Research Question
How can we automatically detect and parallelize common clustering loop patterns using OpenMP while preserving correctness?
03

## Slide 4
PRIOR ART
Related Work & Research Gap
EXISTING WORK
Multicore K-Means parallelization with OpenMP
OpenACC-based K-Means for GPU acceleration
OpenMP Fuzzy C-Means for large-scale datasets
Thread-parallel centroid computation studies
RESEARCH GAP
Manual Only
All approaches rely on hand-coded parallelism
No Auto-Generator
No source-to-source OpenMP pragma inserter exists
No Classification
Clustering loop types are not automatically classified
No Unified Framework
K-Means and FCM require separate ad-hoc solutions
VS
04

## Slide 5
OUR APPROACH
Proposed Solution
AutoCluster-OMP: An end-to-end automatic OpenMP parallelization prototype for clustering workloads.
01
Read Sequential
C Code
02
Detect
For-Loops
03
Classify Loop
Patterns
04
Safety &
Workload Check
05
Generate
OpenMP Code
06
Compile
& Build
07
Benchmark
& Validate
08
Export Reports
& Plots
05

## Slide 6
ARCHITECTURE
System Pipeline
1
Sequential
C Code
Input
2
Loop
Detection
Analyzer
3
Pattern
Classification
Analyzer
4
Safety
Check
Validator
5
OpenMP
Generation
Generator
6
Benchmark
& Validate
Output
IN
OUT
OpenMP C Files
CSV Reports
JSON Analysis
Performance Plots
06

## Slide 7
HARD CLUSTERING
K-Means Auto-Parallelization
SEQUENTIAL CODE
for (int i = 0; i < n; i++) {
...
labels
[i] = best_cluster;
}
AUTO-GENERATED OPENMP
#pragma omp parallel for schedule(static)
for (int i = 0; i < n; i++) {
...
labels
[i] = best_cluster;
}
WHY IT'S SAFE
Each point processed independently — no shared state
Each iteration writes to unique labels[i] memory location
Centroids are read-only during the assignment step
07

## Slide 8
SOFT CLUSTERING
Fuzzy C-Means Auto-Parallelization
SEQUENTIAL CODE
for (int i = 0; i < n; i++) {
for (int c = 0; c < k; c++) {
...
membership[i*k+c] = value;
}
}
AUTO-GENERATED OPENMP
#pragma omp parallel for schedule(static)
for (int i = 0; i < n; i++) {
for (int c = 0; c < k; c++) {
...
membership[i*k+c] = value;
}
}
08
Threads write to different memory cells
Each point owns a separate membership row
No two threads update the same membership[i*k+c]

## Slide 9
SAFETY ENGINE
Loop Classification & Safety
kmeans_assignment_loop
PARALLELIZE
fuzzy_membership_update_loop
PARALLELIZE
centroid_update_loop
WARN
possible_reduction_loop
WARN
unknown_loop
SKIP
UNSAFE EXAMPLE
centroid_counts[cluster]++; centroid_sums[cluster*d+f] +=
points[i*d+f];
⚠ Multiple threads may update the same centroid accumulator simultaneously — causing a race condition.
Safe — auto-parallelized
Warning — manual review needed
Unsafe — skipped
09

## Slide 10
IMPLEMENTATION
Implementation Details
C Kernels
kmeans_seq.c
kmeans_manual_omp.c
kmeans_auto_omp.c
fcm_seq.c
fcm_manual_omp.c
fcm_auto_omp.c
Python Tool Modules
analyzer detects and classifies loops
generator inserts OpenMP pragmas
compiler compiles C files with GCC
benchmark measures runtime and speedup
reports exports CSV / JSON files
plotting generates figures
Main Outputs
→ Auto-generated OpenMP C files
→ Benchmark CSV files
→ Analysis JSON reports
→ Runtime, speedup & efficiency plots
11

## Slide 11
PERFORMANCE DATA
Benchmark Results
5.12x
Peak Speedup
8 threads
80.47%
Runtime Reduction
100%
Correctness
All checksums passed
8
Thread Configs
1, 2, 4, 8 threads
Chart: Speedup vs. Sequential Baseline
| Sequential Baseline,1.00 | K-Means Auto OpenMP,4.37 | Fuzzy C-Means Auto OpenMP,4.32 | Best FCM Schedule Sweep,5.12 | 8 Threads (3.13x)
Speedup | 1 | 0.83 | 1.37 | 2.54 | 3.13
Chart: Runtime Reduction (seconds)
| K-Means Seq,5.732 | K-Means Auto OMP×8,1.311 | FCM Seq,20.952 | FCM Auto OMP×8,4.847 | Best FCM Sweep,4.666
Runtime (s) | 4.281 | 5.188 | 3.131 | 1.683 | 1.369
11

## Slide 12
INSIGHTS
Result Discussion
Chart: Parallel Efficiency by Thread Count
| 1T,100 | 2T,91 | 4T,81 | 8T,55
Efficiency (%) | 100 | 68.5 | 63.5 | 39.1
Amdahl's Law governs the ceiling. The sequential centroid-update phase limits maximum theoretical speedup regardless of thread count.
12
Runtime reduced from 4.281s to 1.369s — a 68% improvement at 8 threads
1-thread OMP was slower (5.188s vs 4.281s) due to OpenMP runtime overhead
Efficiency drops at 8 threads due to Amdahl's Law: remaining sequential sections limit scaling
All OpenMP configurations passed checksum correctness validation

## Slide 13
HORIZON
Limitations & Future Work
CURRENT LIMITATIONS
✗ Pattern-based parser, not a full AST compiler
✗ Best suited for controlled C code patterns
✗ Complex pointer aliasing not fully analyzed
✗ Centroid-update loops require manual review
FUTURE ROADMAP
v2.0
Clang AST Analysis
Replace regex parser with full compiler frontend
v2.1
Auto Centroid Transform
Automatic local-buffer reduction patterns
v3.0
Smart Schedule Selection
Dynamic vs static scheduling based on workload
v4.0
GPU Acceleration
OpenACC and CUDA code generation support
13

## Slide 14
IMPACT
Key Contributions
C1
Source-to-Source Prototype
End-to-end lightweight OpenMP auto-parallelizer
C2
K-Means Loop Detection
Automatic identification of safe assignment loops
C3
FCM Loop Detection
Soft clustering membership-update loop classification
C4
Safety Classification
Red/yellow/green decision engine for race conditions
C5
Workload-Aware Decisions
Parallelization threshold based on loop size
C6
Full Benchmark Suite
Runtime, speedup, efficiency, and correctness metrics
C7
Reproducible Evaluation
CSV and JSON export for research reproducibility
C8
Paper-Ready Plots
Publication-quality performance visualizations
14

## Slide 15
CONCLUSION
AutoCluster-OMP
demonstrates that clustering loop patterns can be detected and
parallelized automatically — without human intervention.
Auto Detection
Safe Parallelism
Correct Output
3.13× Speedup
Zero Race Conditions
Mohamed Yasser Goma · Abdullah Ismail · Mohamed Khaled · Mohamed Saleh · Ahmed Sayed
CSCI465 · Introduction to Parallel Computing
Thank You